## Slide 1
JCESR: One Year Later
George Crabtree
Director, JCESR
Argonne National Laboratory
University of Illinois at Chicago
Outline
Challenges: Transportation and Electricity Grid
Vision, Mission, Legacies
A New Paradigm
Highlights: trace water, solvation, Mg-ion battery
Directions: solvation, metal anodes, novel prototypes, reaction pathways
Basic Energy Sciences Advisory Committee (BESAC)
July 29, 2014
Bethesda, MD

## Slide 2
Energy Demand
The bottleneck for both transitions is
inexpensive, high performance electrical energy storage
Energy Storage Challenges
Chart: 
| Transportation | Non-Electric Industrial | Electricity | Non-Electric Residential and Commercial
 | 0.28 | 0.22 | 0.39 | 0.11
Transportation 28%
Residential & Commercial
Non-electric
11%
Electricity Grid
39%
Industrial
Non-electric
22%
Two biggest energy uses poised
for transformational change
Transportation 28%
  Foreign oil  domestic electricity
  Reduce energy use
  Reduce carbon emissions
Electricity 39%
  Coal  Gas  Wind and Solar
  Greater reliability, resiliency, flexibility
  Replace “just in time” with inventory
2013
EIA Monthly Energy Review Table 2.1 (May 2014)

## Slide 3
Transportation
GRID
$100/kWh
400 Wh/kg 400 Wh/L
800 W/kg 800 W/L
1000 cycles
80% DoD C/5
15 yr calendar life
EUCAR
$100/kWh
95% round-trip efficiency at C/5 rate
7000 cycles C/5
20 yr calendar life
Safety equivalent to a natural gas turbine
JCESR Has Transformative Goals
Vision
Transform transportation and the electricity grid
with high performance, low cost energy storage
Mission
Deliver electrical energy storage with five times the energy density and one-fifth the cost of today’s commercial batteries within five years
Legacies
A library of the fundamental science of the materials and phenomena of energy storage at atomic and molecular levels
Two prototypes, one for transportation and one for the electricity grid, that, when scaled up to manufacturing, have the potential to meet JCESR’s transformative goals
A new paradigm for battery R&D that integrates discovery science, battery design, research prototyping and manufacturing collaboration in a single highly interactive organization

## Slide 4
Why So Aggressive?
Seek transformative outcome
Next generation energy technology demands next generation electricity storage
Bring the community to the rich potential of beyond lithium-ion
Lithium-ion – the best battery technology we have ever seen
  Increases energy density at 5%/yr
  Decreases cost at 8%/yr
. . . but cannot achieve transformative factors of five in cost and performance
JCESR  beyond Lithium-ion

## Slide 5
Multivalent Intercalation
Chemical Transformation
Non-Aqueous Redox Flow
CROSSCUTTING SCIENCE
Systems Analysis and Translation
Cell Design and Prototyping
Commercial Deployment
Battery Design
Research Prototyping
Manufacturing Collaboration
MATERIALS
PROJECT
TDTs
Discovery Science
JCESR Creates a New Paradigm for Battery R&D
++
TECHNO-ECONOMIC MODELING
“Building battery systems on the computer”
ELECTROCHEMICAL DISCOVERY LAB
Wet and dry electrochemical interfaces
Model single crystals
Practical nanoparticles

## Slide 6
Lithium Ion Battery Technology

## Slide 7
JCESR’s Beyond Lithium-ion Concepts
Multivalent Intercalation
Chemical Transformation
Replace monovalent Li+ with
di- or tri-valent ions: Mg++, Al+++, . . .
Double or triple capacity stored and released
Replace intercalation with high energy chemical reaction: Li-S, Li-O, Na-S, . . .
Replace solid electrodes with liquid solutions or suspensions:
lower cost, higher capacity, greater flexibility
Non-aqueous Redox Flow
Black, Adams, Nazar, Adv. Energy Mater 2, 801 (2012)
Yang, Zheng, Cui, Ener Env Sci 5, 1551 (2013)
Mg++
Lithium-ion “Rocking Chair”
Li+ cycles between anode and cathode, storing and releasing energy

## Slide 8
mostly
unknown
transformational
advances
Beyond Lithium Ion Opportunity Space is Large, Unexplored and Rich
Graphite, LiCoO2
LiFePO4, LiMnO2
. . .
Intercalant electrodes
Materials
Systems
Li-ion
Beyond
Li-ion
extensive knowledge
clear pathways to advances
Intercalant
Catholyte
Chemical
Transformation
Liquid
Solid
Intercalant/Alloy
Metal
Anolyte
Li
Mg Al
Bi, Sn, Oxysulfides
Quinoxaline
Metal
Coordination Complexes
Triflate, Tetraborate
Oxide
Phosphate-based ceramics,
Block Co-polymer
Spinel
Layered
Li-O
Li-S
Na-S
Quinoxoline Ferrocence
Polysulfides

## Slide 9
JCESR Approach to Big, Unexplored Beyond Lithium-ion Space
Partners that span the space
  Five national labs
  Five universities, plus faculty from four non-partner universities
  Four private sector companies
Affiliates that represent the community
  45 affiliates at launch
  65 affiliates as of July 2014
New tools define the landscape
  Materials Project / Electrolyte Genome
  Electrochemical Discovery Lab
  Techno-economic Modeling
Battery concepts with multiple implementations
  Multivalent Intercalation
  Chemical Transformation
  Non-aqueous Redox Flow
Parallel research across four functions + frequent communication
Fundamental science and engineering inform strategic directions

## Slide 10
JCESR Team
and Affiliates
45 Affiliates at launch
65 Affiliates July 2014
Affiliates Day
March 19, 2014
Affiliates Newsletter
July 2014

## Slide 11
1-2 YEARS
BTRL - 1
2-5 YEARS
BTRL - 2
2-5 YEARS
BTRL - 3
5-10 YEARS
BTRL – 5 - 6
Battery Technology Readiness Level (BTRL)
Proof-of-concept prototype
Research prototype
Scientific Breakthrough
New class of materials synthesized
Proven performance
in half cells
Proven performance in
lab-scale full cells
Material scale-up, cell testing and scale-up to pack
JCESR
“sweet spot”
Developed collaboratively with
JCI, NASA-Glenn, TARDEC
BTRL - 3
Response to advice from
Governance Committee, ESAC and action item from Oct 1 Management Review

## Slide 12
Multivalent Intercalation
Chemical Transformation
Non-Aqueous Redox Flow
CROSSCUTTING SCIENCE
Systems Analysis and Translation
Cell Design and Prototyping
Commercial Deployment
Quantifying the promise of Li-air batteries (with GM)
Gallagher et al, Energy and Environmental Science (2014) DOI:10.1039/C3EE43870H
Link to Community
New IP
Infinite current collector
Industry-science collaboration
Six projects of interest to JCI
MOU with NASA-Glenn
Battery Design
Research Prototyping
Discovery Science
Manufacturing
Collaboration
JCESR Achieves Across the Science-Manufacturing Spectrum
System Mass for 100 kWhuse (kg)
System Volume for 100 kWhuse (L)
Useable Specific Energy (Whuse/kg)
Useable Energy Density (Whuse/L)
Tesla Model S
85 kWhuse
Nissan Leaf
22 kWhuse
Li/LMRNMC
Si/LMRNMC
Gr/LMRNMC
Gr/NMC333
Li/O2 closed
Li/O2 open
discharged
charged
Li/LMRNMC
Gr/NMC333
Theoretical kWh/kg
Theoretical kWh/L
1
2
3
4
1
2
3
Li/O2
Trace water catalyzes lithium peroxide electrochemistry
EDL+Electrolyte Genome
Jirkovský et al, Science (submitted)
V
2 DBBB
2 [DBBB+A-]
TMQ
Trimethylquinoxaline
TMQ2- [C+]2
2e-
2C+
2e-
All Organic Redox Flow
Non-aqueous Redox Flow + Electrolyte Genome
Brushett, Zhang et al (MIT, ANL)
BF4-
+
TMQ
BF4-
10x electrochemical activity
First year summary + more highlights
www.jcesr.org

## Slide 13
Toward a Multivalent Intercalation Battery
Challenges
Mobility of ++ ions in cathode
Solvation – desolvation
Stable electrolyte
Compatible anode, electrolyte, cathode
Only one demonstrated system
Mg-chloroaluminate-Mo6S8
(Aurbach 2000)
Metal
Anode
Intercalation Cathode
Electrolyte
Mg0  Mg2+ + 2e-
High Li+ diffusion ≠
high MV diffusion
Coordination environment controls diffusion barrier
Tetrahedral octahedral  tetrahedral
Ca++ has surprisingly low mobility barrier
Early stage prototype
Compatible
anode-electrolyte-cathode
Mg metal anode
Diglyme electrolyte
V2O5 cathode
Mobility in Mn2O4 Cathode
Mg++ Solvation Shell
First Fully Functional Mg++ Battery since 2000
Energy barriers for MV ion diffusion in Mn2O4 spinel
Materials Project
Ca++
Mg++
Li+
Experiment
Computation
······ Mg-solvent
- - - Mg-anion
Mg++
Diglyme
Diglyme
TFSI−
(r / Å)
1
2
3
4
5
6
7
Distribution of atomic distances
Controls
• Chemical reactions in electrolyte
• Interfacial ion exchange
• Mobility in electrolyte
Experiment: APS x-ray diffraction
Simulation: Electrolyte Genome
Pair Distribution Function
Quantifies anion presence in solvation shell
Lapidus et al, submitted (PCCP)
First year summary + more highlights
www.jcesr.org

## Slide 14
Priority Research Areas
Solvation/de-solvation structure and transfer dynamics
Metal Anodes
Robust surfaces over
multiple solution/deposition cycles
Park et al, Nature Scientific Reports doi:10.1038/srep03815
Solution/deposition dynamics, surface degradation,
dendrite growth
Critical to battery science and technology strategies
Rich opportunities for in situ, time-resolved, multi-modal characterization, predictive theory and multiscale modeling
fully solvated ion
In bulk electrolyte
partially solvated ion at interface
-
Electrolyte
30-50 nm
Solid-Electrolyte Interphase
Kang Xu ARL
Thackeray,ANL
+
Electrode
+
+
+
+
+
+
Novel Prototyping Concepts
Gravity Induced Flow Cell
Molecular Understanding
of Reaction Pathways and Energetics
Lithium-Sulfur Batteries
Electrolyte Genome / EDL
Li-polysulfide Semi-Flow
Concept
Y. Yang, G. Zheng, and Y. Cui, Energy & Environmental Science, 6, 1552 (2013)

## Slide 15
Perspective
Vision: Transform transportation and electricity grid with high performance, low cost energy storage
Mission: Deliver electrical energy storage with five times the energy density and one-fifth the cost
 Beyond lithium ion
Legacies:
A library of the fundamental science of the materials and phenomena of energy storage at atomic and molecular levels
Two prototypes, one for transportation and one for the electricity grid, that, when scaled up to manufacturing, have the potential to meet JCESR’s performance and cost goals
A new paradigm for battery R&D that integrates discovery science, battery design, research prototyping and manufacturing collaboration in a single highly interactive organization
A bold new approach to battery R&D
Accelerate the pace of discovery and innovation
Bring the community to the beyond lithium-ion opportunity
More on JCESR website
www.jcesr.org